## Slide 1
>>>
No Dev? No Problem. pySROS for Network Engineers
Setup · Interactive Mode · Your First Scripts
No coding background needed — if you know the CLI, you're ready

## Slide 2
What We'll Cover
01
Check Python
Confirm Python 3 is ready to go
02
Create a Virtual Environment
Isolate your project in a clean sandbox
03
Activate & Install pySROS
pip install in one command
04
Python Interactive Mode
Connect and explore YANG paths live
05
Make Your First Query
Pull real data from the router

## Slide 3
What is a Virtual Environment?
Think of it as...
A clean, isolated folder that contains its own Python installation and packages — completely separate from everything else on your machine.
Like having a dedicated lab bench for each project — no cross-contamination.
Why it matters
No conflicts between projects
Easy to delete and start fresh
Share exact dependencies with teammates
Keeps your system Python clean

## Slide 4
Steps 1 & 2: Check Python · Create venv
STEP 1
Check Python is installed
$ python3 --version
STEP 2
Create a Virtual Environment
$ python3 -m venv pysros-env
This creates a folder called pysros-env containing a self-contained Python environment.

## Slide 5
Step 3: Activate & Install pySROS
ACTIVATE
source pysros-env/bin/activate
Your prompt changes to: (pysros-env) user@host:~$ ← You're now inside the sandbox!
INSTALL
pip install pysros
Verify the install:
pip show pysros

## Slide 6
Step 4: Enter Python Interactive Mode
With your venv active, just type:
Terminal
$ python3
Python 3.10.12 (default, ...)
Type "help", "copyright" or "license" for more information.
>>>
The >>> prompt means Python is listening. Type a line, hit Enter, get an instant response. Perfect for exploring before writing a full script.

## Slide 7
Step 5: Connect & Query the Router
Python Interactive Session
>>> from pysros.management import connect
>>> connection = connect(
... host="192.168.1.1", username="admin",
... password="admin", hostkey_verify=False)
>>> connection.running.get("/nokia-conf:configure/system/name")
'SR-OS-DEMO-ROUTER'
>>> connection.running.get("/nokia-conf:configure/system/location")
'Amsterdam, Netherlands'

## Slide 8
Key Concept: YANG Paths
The path you pass to .get() is a YANG model path — this is what 'Model Driven' means.
/nokia-conf:configure/system/name
Module prefix
Container
Leaf (the value)
Common paths to try
/nokia-conf:configure/system/name
System hostname
/nokia-conf:configure/system/location
Physical location
/nokia-conf:configure/system/contact
Contact info
/nokia-state:state/system/version/version-number
Software version

## Slide 9
Quick Reference
python3 -m venv pysros-env
Create the virtual environment
source pysros-env/bin/activate
Activate it
pip install pysros
Install pySROS
python3
Enter interactive mode
from pysros.management import connect
Import pySROS
connection.running.get("..path..")
Query the router
deactivate
Exit the environment
pySROS Documentation: https://network.developer.nokia.com/sr/learn/pysros