## Slide 1
.py
No Dev? No Problem.
pySROS Scripting for Network Engineers
Out-of-Box · On-Box · Config Changes · Real-World Use Cases
No coding background needed — if you know the CLI, you're ready

## Slide 2
Today's Agenda
5 min
Quick Recap
MDM + pySROS refresher
20 min
Setup
venv · install · interactive mode
20 min
Out-of-Box Scripts
Remote NETCONF — interface status & BGP
15 min
On-Box Scripts
Running Python directly on SR OS
15 min
Config Changes
set / edit operations via pySROS
10 min
Real-World Use Cases
Bulk config change across multiple nodes
5 min
Q&A
Open floor

## Slide 3
Interactive Mode — Import & Connect
>>> mode
Terminal — python3
$ python3
Python 3.10.12 (default ...)
Type "help" for more info.
>>> from pysros.management import connect
>>> conn = connect(host="clab-srexperts-pe1",
... username="admin", password="admin",
... hostkey_verify=False)
>>> # No error = session established!
No error after connect() = session is live. Now start querying the router.

## Slide 4
Interactive Mode — Your First Queries
>>> mode
Terminal — live YANG queries
>>> conn.running.get("/nokia-conf:configure/system/name")
'SR-OS-DEMO-ROUTER'
>>> conn.running.get("/nokia-conf:configure/system/location")
'Amsterdam, Netherlands'
>>> conn.running.get("/nokia-conf:configure/system/contact")
'noc@example.com'
>>> name = conn.running.get("/nokia-conf:configure/system/name")
>>> print(name)
SR-OS-DEMO-ROUTER
>>> conn.disconnect()
Path = YANG tree
Just change the end of the path to get different data
.data = raw value
The object returned has a .data property for the value
exit() when done
Type exit() or Ctrl+D to leave interactive mode

## Slide 5
Interactive Mode — Drilling Into a Specific Neighbor
>>> mode
Approach 1 — get all, then index
>>> n = neighbors["192.168.1.1"]
>>> for k in n.keys(): print(k)
ip-address
statistics
graceful-restart
>>> # session-state is inside
>>> # the statistics container
>>> n["statistics"]["session-state"].data
'Established'
>>> n["statistics"]["last-state"].data
'Active'
>>> n["statistics"]["last-event"].data
'recvOpen'
>>> n["statistics"]["received-paths"].data
Approach 2 — direct YANG path
>>> # Full YANG path — direct
>>> conn.running.get(
... "/nokia-state:state/router
... [router-name="Base"]
... /bgp/neighbor
... [ip-address="192.168.1.1"]
... /statistics/session-state")
Leaf('Established')
>>>
>>> # Other useful fields:
>>> # /statistics/last-state
>>> # /statistics/last-event
>>> # /statistics/received-paths
session-state lives inside statistics, not at the top level. Use .keys() at each level to navigate — sparse fields only appear when populated.

## Slide 6
01
Out-of-Box Scripts
Remote execution via NETCONF from your laptop or automation server

## Slide 7
How Out-of-Box Execution Works
Your Machine
Python script
pySROS installed
NETCONF / SSH
Port 830
Encrypted session
SR OS Node
Containerlab
vSR OS
▶
▶
connect() Opens a NETCONF session — you pass host, username, password
connection.running.get(path) Reads live config or state data from the YANG tree
connection.disconnect() Always clean up your session when done
hostkey_verify=False Fine for lab/Containerlab — use proper keys in production

## Slide 8
Script 1 — Interface Status
out-of-box
01_interface_status.py
from pysros.management import connect
def main():
conn = connect(host="clab-srexperts-pe1",
username="admin", password="admin",
hostkey_verify=False)
ports = conn.running.get("/nokia-state:state/port")
for port_id, port_data in ports.items():
oper = port_data.get("oper-state", {}).data
admin = port_data.get("admin-state", {}).data
print(f"{port_id:<15} admin={admin:<5} oper={oper}")
conn.disconnect()
Sample output: 1/1/1 admin=up oper=up 1/1/2 admin=up oper=down

## Slide 9
Script 2 — BGP Neighbor State
out-of-box
02_bgp_neighbors.py
from pysros.management import connect
BGP_PATH = (
"/nokia-state:state/router[router-name=Base]"
"/bgp/neighbor"
)
def main():
conn = connect(host="clab-srexperts-pe1",
username="admin", password="admin",
hostkey_verify=False)
neighbors = conn.running.get(BGP_PATH)
Sample output: Neighbor 192.168.1.1 State: established Neighbor 10.0.0.2 State: idle

## Slide 10
02
On-Box Scripts
Python running directly on the SR OS node — no external connection needed

## Slide 11
Out-of-Box vs On-Box
OUT-OF-BOX
Runs on your laptop or CI server
Needs network access to router
Uses NETCONF over SSH (port 830)
Full Python ecosystem available
Great for automation pipelines
connect() with host= parameter
ON-BOX
Runs inside SR OS Python VM
No external connectivity needed
connect() with no arguments
Triggered by EEM / cron / CLI
Limited to pySROS + stdlib
Lowest latency to router data

## Slide 12
The Key Difference — connect()
Out-of-Box — with host/credentials
conn = connect(host="clab-srexperts-pe1", username="admin",
password="admin", hostkey_verify=False)
On-Box — no arguments needed
conn = connect()
When running on-box, pySROS connects to the local SR OS instance automatically. The rest of your script — .get(), .set() — is identical. This means the same script logic works both ways with just a one-line change.

## Slide 13
Script 3 — On-Box Interface Check
on-box
03_onbox_interface_check.py
from pysros.management import connect
from pysros.pprint import Table
def main():
conn = connect() # on-box: no args needed
ports = conn.running.get("/nokia-state:state/port")
rows = []
for port_id, port_data in ports.items():
oper = port_data.get("oper-state", {}).data
admin = port_data.get("admin-state", {}).data
rows.append([port_id, admin, oper])
Deploy: copy script to SR OS → /cf3:/scripts/ | Run: pyexec /cf3:/scripts/03_onbox_interface_check.py

## Slide 14
03
Config Changes
set() and candidate config operations — making the router do what you want

## Slide 15
Reading vs Writing — The Two Operations
READ (get)
conn.running.get("/nokia-conf:configure/system/name")
Reads from the running datastore. Returns a pySROS Container or Leaf object.
WRITE (set)
conn.candidate.set(
"/nokia-conf:configure/system/name",
"new-router-name"
)
Writes to the candidate datastore. Changes only take effect after commit().
COMMIT
conn.candidate.commit()
Applies candidate config to running. Use lock=True to prevent concurrent changes.

## Slide 16
Script 4 — Set System Description
config change
04_set_description.py
from pysros.management import connect
def set_port_description(conn, port, description):
path = f"/nokia-conf:configure/port[port-id={port}]"
"/description"
conn.candidate.set(path, description)
def main():
conn = connect(host="clab-srexperts-pe1",
username="admin", password="admin",
hostkey_verify=False)
set_port_description(conn, "1/1/1", "Uplink to Core-01")
set_port_description(conn, "1/1/2", "Peering Link - AS65001")

## Slide 17
04
Real-World Use Cases
Bulk config changes across multiple nodes — the power of automation

## Slide 18
Script 5 — Bulk Config Across Multiple Nodes
real-world
05_bulk_config.py
from pysros.management import connect
NODES = [
{"host": "clab-srexperts-pe1", "name": "PE1"},
{"host": "clab-srexperts-pe2", "name": "PE2"},
{"host": "clab-srexperts-p1", "name": "P1" },
]
def apply_ntp_server(conn, ntp_ip):
path = f"/nokia-conf:configure/system/time/ntp"
f"/server[ip-address={ntp_ip}]/prefer"
conn.candidate.set(path, True)
conn.candidate.commit()
def main():
NTP = "10.0.0.1"
for node in NODES:

## Slide 19
What You Can Now Do
🌐
Run scripts remotely
Connect to any SR OS node from your machine via NETCONF
📦
Deploy on-box scripts
Drop Python directly onto SR OS — no external host needed
✏
Push config changes
Use set() + commit() to change anything in the YANG tree
🔧
Automate at scale
Loop across a node list — change 1 or 100 routers at once